## Slide 1
REVOLUTIONIZING HEALTH CARE
Patient Monitoring System for Post-Operative Care
Home
About Us
Service
Contact
CARE CONNECT.

## Slide 2
Introduction
Home
About Us
Service
Contact
Post-operative patients require continuous monitoring of vital signs (pulse, BP, blood sugar, etc.).
Current solutions are expensive, bulky, or limited to specific vitals.
Need for an affordable, integrated system with real-time mobile app access
www.reallygreatsite.com
CARE CONNECT.

## Slide 3
Home
About Us
Service
Contact
Apps Main
Features
CARE CONNECT
Develop a hardware-software system to monitor vital signs post-operation.
Non-invasive sensors for pulse, BP, temperature, and (optionally) blood sugar.
Mobile app for real-time data display and alerts. Wireless connectivity (Bluetooth/Wi-Fi).
key features:

## Slide 4
Home
About Us
Service
Contact
CARE CONNECT
System
Architecture
Hardware:
Sensors (MAX30102 for pulse, DS18B20 for temperature), Arduino/ESP32 microcontroller, Bluetooth module.
Software:
Mobile app (Flutter) for data visualization and alerts.
Connectivity:
Bluetooth for real-time data transfer.
Cloud (Optional):
Store historical data for analysis.
CARE CONNECT
CARE CONNECT
CARE CONNECT

## Slide 5
Home
About Us
Service
Contact
Hardware
Design
CARE CONNECT
Sensors:
Pulse Oximeter (MAX30102): Measures heart rate and SpO2.
Temperature (DS18B20): Non-invasive skin temperature.
BP Module: Simulated or integrated with off-the-shelf sensors.
Microcontroller: Arduino Uno/ESP32 for data processing. Power: Battery-operated for portability

## Slide 6
Home
About Us
Service
Contact
SOFTWARE
DESIGN
CARE CONNECT.
CARE CONNECT.
  Mobile app(Flutter):
Dashboard: Real-time vitals display with graphs.
Alerts: Notifications for abnormal readings (e.g., pulse > 100 bpm). History: View past data trends.
  Data Processing: Moving average filter to reduce noise.
  Security: Encrypted data transmission (TLS).

## Slide 7
Home
About Us
Service
Contact
Data Processing
  Collection: Read sensor data every 5 seconds.
  Filtering: Moving average to smooth noise (e.g., average 10 pulse readings).
  Transmission: Send JSON data (‘”pulse”: 75, ”temp”: 36.5‘) via Bluetooth.
Ensures accurate, reliable vital signs for medical use.
CARE CONNECT.

## Slide 8
Home
About Us
Service
Contact
Hardware Software Integration
  Pairing: Bluetooth connection between microcontroller and app.
  Real-Time Sync: Data updates every 5 seconds on app.
  Error Handling: Local buffering if connection drops. Tested for low latency and accuracy.

## Slide 9
Home
About Us
Service
Contact
Impact and Novelty
  Impact: Improves post-operative care with real-time monitoring. Affordable and portable for home/hospital use. Empowers patients and doctors with data.
  Novelty: Integrates multiple vitals in a single device, open-source potential.
  Compared to Existing: Unlike Fitbit or Dexcom, aims for all-in-one monitoring.

## Slide 10
Home
About Us
Service
Contact
Future steps and
Demo
  Next Steps: Add non-invasive glucose monitoring. Seek regulatory approval (FDA/CE). Pilot testing in hospitals.
  Demo: Live showcase of pulse and temperature monitoring on mobile app.

## Slide 11
Home
About Us
Service
Contact
How to
Subscribe
3.submit
1. Visit our website or mobile app
2.Fill the patient details
CARE CONNECT.
CARE CONNECT.
CARE CONNECT.

## Slide 12
www.reallygreatsite.com
Home
About Us
Service
Contact
Download
Now!
Care Connect